## Slide 1: CS 341 Lab 4
Fall 2020

## Slide 2: Lab 4
Goal: investigate memory mapped I/O
Determine which bits in memory control pin 13
Blink an LED (as we did in lab 1) but without using digitalWrite()

## Slide 4: Memory Mapped I/O
There is a little bit of space allocated for each of the pins on the Arduino
We can access this memory without any special functions such as in() and out()
Pins

## Slide 5: Organization of Pins
bits are organized by purpose, not by pin
Data Register – where we write to
Data Direction Register – 0 for reading, 1 for writing
Input Pins – where we read from
Digital Pin 3’s Bits

## Slide 6: Example
How can we access PIND5?
Create a pointer to address 0x29
  dereference it
  Shift 5 bits to the right
  Use a bitmask to see only PIND5
char *example = (char *) 0x29;
int theBit = (*example >> 5) & 1;
Serial.println(theBit, BIN);
// will return 1 or 0

## Slide 7: Interfacing with a digital pin
Using provided functions
pinMode(int pin, OUTPUT);
pinMode(int pin, INPUT);
digitalWrite(int pin, HIGH);
digitalWrite(int pin, LOW);
digitalRead(int pin);
Directly using memory addresses
Set data direction bit to 1
Set data direction bit to 0
Set data bit to 1
Set data bit to 0
Check value of input bit

## Slide 8: Blinking the LED manually
Let’s say that the address for writing to pin 7 is 0x50 and the correct bit is the 6th bit
  0100 00002
Then, this code sets pin 7 to HIGH
And this code turns pin 7 on and off for 1 second each

## Slide 9: Provided Functions
void displayRAM(char *start, char *endd, bool hex)
  Same as we saw in lab 2
  Example output:
    020: 00 00 00 00 20 00 00 00 00 01 00 00 00 00 00 00
void displayBits(char *address)
  Prints an address in hex
  Example output:
    0x100: 1001111