## Slide 1: CS 341 Lab 5
Fall 2020

## Slide 2: Lab 5
Goal: interface with a Liquid-Crystal Display
Scroll text across the screen
Play noise on a piezo speaker

## Slide 3
Brightness (2 pins)
Reading & Writing
Clock
Data mode
Display Contrast
Ground
Power
Register Selection
An LCD Screen

## Slide 4: <LiquidCrystal.h>
Provides a list of functions to abstract all those pins away
lcd.begin(int columns, int rows);
lcd.setCursor(int column, int row);
lcd.print(char[] data);

## Slide 5: Potentiometer
Variable resistor
We can turn the knob to vary how much current goes through
  In this lab, we’ll use it to control the contrast

## Slide 6: Piezo Speaker
Old fashioned speaker
// turn on the buzzer for a tone =1500 hz
tone(buzzer,1500);
delay(10);
// turn the buzzer off
noTone(buzzer);

## Slide 7: Lab 5
Complete the circuit
Implement a circular buffer
“Welcome CS341 Students! ” Then you show:
“elcome CS341 Students! W”. Then you show:
“lcome CS341 Students! We” and so on.