## Slide 1: CS 341 Lab 8
Fall 2020

## Slide 2: Lab 8
Goal: learn about waves and create a frequency meter

## Slide 3: Waves
Pulse Width: how long the signal remains HIGH
Period: The time it takes for the wave to repeat
Frequency: 1/Period
  We can think of frequency as a measure of how dense the wave is

## Slide 4: Function Generator
Outputs a wave-like electrical signal
Settings:
  Frequency: how many times the wave will be repeated in 1 second
  Amplitude: The difference in voltage between the top of the wave and the bottom of the wave
  DC Offset: the voltage amount that the wave is centered at
  Function: change between rectangular, smooth, or triangular wave

## Slide 5: Oscilloscope
Display for visualizing waves

## Slide 6: Part 1 (optional)
Experiment with the function generator and oscilloscope
If the relationship between frequency, period, and pulse width is still a bit confusing, this is a good way to get some intuition

## Slide 7: Part 2
Create an Arduino program that reads a digital signal and calculates:
  Period
  Frequency
Some tips
  Display numbers in seconds
  Serial.println(frequency, 5);
  Be careful of division between two integers