## Slide 1: CS 341 Lab 6
Fall 2020

## Slide 2: Lab 6
Goal: create an outdoor light for a driveway or parking lot
motion sensor to detect a car or person
light sensor to determine whether it is dark or not

## Slide 3: Infrared Motion Sensor
Detects motion by looking at changes in heat
gives us a digital signal
  1 = something detected
  0 = nothing detected

## Slide 4: Photoresistor
A variable resistor that changes based on light detected
To read it, we will need an analog input

## Slide 5: Analog Pins
Read in a value between 0V and 5V
In code, this is interpreted as a value between 0 and 1023
Can also be used as additional digital pins
Example:
  analogRead(A0);

## Slide 6: Lab 6
Complete the circuit
Implement the logic in loop()
  Loop() {
  if (motion) {
  if (light < 200) {
  // light bulb on
  }
  } else {
  //turn the light off if there's no motion
  }
  delay(200);
  }