## Slide 1: CS 341 Lab 3
Fall 2020

## Slide 2: Lab 3
writing a checksum function to check whether our configuration memory has been modified
Make use of bitwise operators

## Slide 3: EEPROM Functions
EEPROM.read(int address)
EEPROM.write(int address, int value)
EEPROM.write(5, 0x41);
EEPROM.read(5); //returns ‘A’

## Slide 4: Bitwise Operators
operate on all numbers, but easiest to see how they work with binary numbers
Exclusive Or (also know as XOR)
  00112 ^ 01012 = 01102
Logical Not (also known as compliment)
~ 01012 = 10102
XOR

## Slide 5: A Simple CheckSum Algorithm
Purpose: checking whether data was corrupted while downloading, transferring, etc
Works by performing an operation on some memory addresses, and storing the result to compare with later
CheckSum Algorithm
  10102 ^ 11112 = 01012
  01012 ^ 11002 = 10012
  10012 ^ 01002 = 11012
  ~11012 = 00102
Index | Value
0 | 1010
1 | 1111
2 | 1100
3 | 0100
4 | 
0010