## Slide 1: CS 341 Lab 7
Fall 2020

## Slide 2: Lab 7
Goal: control a 7-segment display
We will use an integrated circuit to make our code simpler

## Slide 3: 7 Segment Display
Displays numbers by on and turning off 7 LEDs
We need 7 digital inputs to control it
Example: What pins should we turn on to display 7?
  Answer: a, b, c

## Slide 4: Decoder
We can reduce the number of digital inputs to 4 by using a decoder
It takes in a four-bit input and outputs the correct 7-bit signal
Example: 7
  7 in binary is 01112
  Input 0111 to decoder
  Output 1110000
  We see 7 on display
4 Digital Pins
Decoder

## Slide 5: Decoder

## Slide 6: Lab 7
Complete the circuit as provided
Create a counter that starts at 0, and counts up to 9, it should then loop back to 0