## Slide 1: CS 341 Lab 9
Fall 2020

## Slide 2: Lab 9
Goal: Determine whether an object is moving closer or away

## Slide 3: Velocity
Positive or Negative?:
  We pick an orientation and stick with it
  In the lab we’ll call movement away from the sensor positive
Distance d

## Slide 4: Sonar

## Slide 5: Distance Sensor
inputs a digital input
  High means send out a signal
  Low means don’t send a signal
outputs a digital signal
  The length of this signal is equal to how long the it took to get a response
Make sure to use the sensor with 3 pins (not 4)

## Slide 6: Ping()
int ping(int pingPin) {
int duration;
pinMode(pingPin, OUTPUT);
digitalWrite(pingPin, LOW);
delayMicroseconds(2);
digitalWrite(pingPin, HIGH);
delayMicroseconds(5);
digitalWrite(pingPin, LOW);
pinMode(pingPin, INPUT);
duration = pulseIn(pingPin, HIGH);
return duration / 29 / 2;
}
PulseIn
  Returns the pulse width (length of time in ms a digital pin is high for)
Analog input
  Value between [0, 1023] based on voltage in [0, 5V]
Send a signal out
Record time
Divide by Vsound-1
Divide by 2

## Slide 7: Lab 9
The starter code already finds the distance of an object
use the ping() function to estimate the velocity over time
Suggestion: calculate velocity as a float